## Slide 1: Support
Tools for Effective First-Level Support

## Slide 2: Program
Intro
3-5

## Slide 3: Intro
Levels of support

## Slide 4
Cater Solutions to the needs of your Merchants
Use context-based help and guidance for more effective customer support
Help train your merchants to try simple fixes or provide the right information

## Slide 5
Getting Merchants Started
Context-Based Issues
In-Depth Support
Quick Fixes
Setup and basic knowledge
First line of defense
Situational errors and FAQs
Handpoint assistance
Levels of Support

## Slide 6: Get Started
Setup and Basic Knowledge

## Slide 7: Basic Training
Ensure that your merchants are knowledgeable about the products they are using.
User guides
Card reader care guidelines
Device pairing tips

## Slide 8: First-Time Setup
Tools
Card Reader User Manuals
Handpoint mPOS app guides for both Android and iOS
Commonly asked questions
Detailed error lists

## Slide 9: Card Reader Care
  It’s very important to keep the card reader charged with regular use and in storage
  Letting the battery deplete could wipe the stored encryption keys
  The only solution for this is to return the card reader and order a replacement
  Don’t let this happen.
  Card reader storage information pamphlet (pdf)

## Slide 10: Device Pairing
  Pairing should be easy with the HiLite.
  It might seem obvious, but first make sure that Bluetooth is enabled.
  You can connect through the Handpoint App or through the device’s settings
  A: Yes, one at a time. Each time you connect the card reader to a new device you need to register it according to the POS app’s instructions.
Q: Can I pair more than one phone with my card reader?

## Slide 11: Having problems with pairing?
  Restart the mobile device and the card reader.
  Pair through the device settings instead of the app
  If using an iPhone, it may be necessary to first un-pair the card reader with the phone before attempting to pair with another

## Slide 12: Quick Fixes
Before you call…

## Slide 13: Simple Solutions
Many customers
Call too soon
Are experiencing problems that can be solved with simple, general fixes
Try the simple solutions first.
“Have you tried turning it off and on again?”

## Slide 14: Sometimes simple works best
Before anything else:
Restart the Phone
Disconnect and Re-connect the Bluetooth
Restart the network connection
Restart the Card Reader

## Slide 15: Flash Reset
Performing a flash reset:
    Press C and ← (back button)
    Enter password: 746723 and press OK
    Scroll menu using ↓ (down arrow) to Config and press OK
    Select “RESET FLASH“ and press OK
    Scroll down to “Save and Reset“ and press OK
    The card reader should now restart
A good go-to solution for:
Re-using a device
Processing errors
Loop errors
General malfunctions
Can be found here on our Confluence site
Remember: always check for software updates after a flash reset

## Slide 16: Context-Based
Cause-Effect troubleshooting

## Slide 17: Tips
It’s important to know:
If a card reader is set up in the Handpoint TMS, it won’t be ready the same day
When Handpoint receives an order, it will only be delivered the next day if the order was received before 1:30pm GMT
If a card reader is set up with a Merchant, who then changes their name, the device will need to be re-registered with Handpoint and updated in the Handpoint app settings.
Info that will make it easier for Handpoint to help you get started

## Slide 18: Common Error Messages
Invalid BPK
Comm. Error
Network Error/Send Error
Processing Error
Device Not Initialized
These messages will likely be among the most common when merchants seek support assistance.

## Slide 19: “Invalid BPK”
Critical error
The card reader is in tamper mode
Happens when:
  it’s dropped
  someone tries to open the case
  or the battery becomes depleted
Needs to be returned to secure facility and replaced
Refer to the card reader storage pamphlet for info on how to prevent this

## Slide 20: “Comm. Error”
There was an error in communication between the card reader and the mPOS app
Ensure that you are within bluetooth range
Frequently, trying again works
Restarting the card reader sometimes solves it
If, after repeated tries, it still doesn’t work, contact Handpoint

## Slide 21: Network Error/Send Error
Credit card transaction processing system (bureau) at Handpoint is temporarily out of service Contact Handpoint Frequently means that the internet connection is inadequate Either the 3G is too weak or the merchant’s Wifi is not working Check internet settings

## Slide 22: Processing Error
An unexpected error was encountered during transaction processing.
Please retry the operation.
If the issue persists please contact support

## Slide 23: “Device Not Initialized”
The card reader has not fetched its config during the initial setup.
Try updating the card reader and if the problem persists notify Handpoint
There was an error registering the device in the Handpoint system.
Contact Handpoint immediately to resolve this.

## Slide 24: In-Depth
Higher-level support

## Slide 25: Support Mode
On Android:
  After entering your passcode and logging into the app, swipe to the left to reach the menu.
  Scroll down to the Support Mode option and uncheck the box if it’s enabled.
On iOS:
  After entering your passcode and logging into the app, swipe to the left to reach the menu.
  Scroll down until you see the Support Mode option and disable it if it’s enabled.
For us to help, we need the message logs. This is how to start gathering them using the app’s support mode.
The card reader will take longer to respond when in Support Mode

## Slide 26: Contacting Handpoint
  Serial number of device
  Company/merchant name
  Time and date of error
  Error/Issue description
  Type of operating system
  Error/issue logs
  Type of internet connection, if applicable
  Handpoint SDK version
  Type of Handpoint device
  What was happening when the error occurred?
If all else fails, get in touch with us.
We will need this basic information in order to provide support assistance.
This information is required (when applicable)
This list can also be found on our Confluence site

## Slide 27
Limitations
Good to know

## Slide 28
  What is it?
  A server update done at the end of each day.
  What does it do?
  Registers vital changes regarding the service.
SPS update
  Some changes are dependent on the update and will not be active until a SPS update has taken place.

## Slide 29
Keep in mind
  When setting up a new merchant in TPOS so they can handle payments
  When setting up/adding a device so it can be registered to that merchant
  When there are any changes to the customer agreement
  In order to make changes to the terminal ID (TID)
  In order to make changes to the card reader
An SPS Update is required:
  Note: Changes to the EFT client and in the customer outlet are not dependent on an SPS update.

## Slide 30
For more information, visit our Support Space on Confluence